## Slide 1: UW System Network Operations Metrics
Patrick Christian
Mike Schlicht
9/23/2015

## Slide 2
What gets measured gets managed

## Slide 3: Significant event summary
UW/WiscNet network engineer deployment activities caused ~4 hours of campus "isolation" from world
~16 hour electrical (line card failure) event in IA City
~38.75 hours of commercial circuit downtime - particularly UW-Platteville's backup connection
Portion of fiber to UW-Platteville was not buried resulting in a 10.3 hour fiber repair
Several commercial power outages - most with minimal impact due to investment in DC power systems

## Slide 4: Significant event summary
Various HVAC issues in pedestals & UWC locations
Significant unplanned fiber (cut) repairs
  UWEC - UWC-BarronCO (~3.5 days) (weather decision)
  Ames, IA (10 hours)
  Kenosha (4.5 hours)
Several campuses had significant LAN issues that are not included in these statistics

## Slide 5: Workload metrics
~6 months of activity after deployments
202 total # of tickets (calls)
  72 planned events
  130 unplanned events
…stated another way
  94 service affecting events
  108 non-service affecting events
Service affecting events = # of times when any component of the network operated in a degraded state

## Slide 6: FY15 network availability
Many ways to calculate including planned + unplanned events vs. just unplanned vs. actual isolation of a campus network from world
99.947% availability

## Slide 7: Root cause analysis
Chart: Frequency distribution of network event root causes
| Fiber | Facilities | CPE | Operations | Hardware | Circuits | Software | Misc
Series 1 | 56 | 40 | 30 | 20 | 19 | 18 | 15 | 4
Series 2
Series 3

## Slide 8: Root cause analysis
Chart: UW-System network cumulative number of minutes per root cause type
| Fiber | Facilities | CPE | Operations | Hardware | Circuits | Software | Misc
Duration (in min) | 17130 | 2140 | 15 | 202 | 1314 | 4263 | 41 | 1

## Slide 9: Questions?
  patrick.christian@wisc.edu
  mschlicht@uwsa.edu
Notes: Procure optical hardware