## Slide 1: Juniper update
Michael Hare
2015/09/23
UW System Network

## Slide 2: Overview
Juniper updates
SDN/orchestration
Roadmap
Feature updates
Uptime: BFD, IP fast reroute aka LFA [loop free alternative]
MPLS and E-VPN

## Slide 3: Juniper SDN/orchestration
contrail: Openstack based network orchestration software
Mix of MPLS/routing/acl orchestration to
  replace vlans/vrfs
  pushes MPLS PE like functions to hypervisor
  enables "network function virtualization -> NFV"
    pushing state decisions to external x86 sdks [firewall, ids] by orchestrated config

## Slide 4: Juniper Roadmap
Surprise: lots of newer, denser linecards coming
Mx2010 core: we currently use MPC4E 2x100 + 8x10 and 32x10. They can do roughly 240G full duplex [slightly oversubscribed]
Our current fabric cards support 800G [8 x 100G] per linecard.
No immediate plans to change course; changing course is expensive [sparing]
JUNOs can run inside x86 [route reflector] and they have a virtual forwarding hardware implementation [x86 server = JUNOs router]. Interesting for lab work
A chassis larger than an mx104 but smaller than an mx240 is due mid to late 2016. May be an ideal replacement for locations where we've deployed and mx104 and a Cisco 4500X or for centralized datacenter.

## Slide 5: Uptime: Tools for speeding convergence
Loop free alternative routes enabled: IGP precomputes [not 100% coverage] a backup path and pre-installs the route in the forwarding table
BFD to providers: WRIPs and I2 yes, transit not so much. As we are not directly connected to transit provider routers, this can cause brief, partial blackholing during WAN events [60 to 90s] such as fiber cuts between Milwaukee and Chicago or Madison and Chicago via BOREAS [Minnesota, Iowa].

## Slide 6: MPLS deployment and E-VPN update
MPLS ‘more fully’ deployed on UW System Network this summer
  Several point to point layer 2 MPLS VPNs [l2circuit] in production since last year.
  No layer 3 MPLS VPNs in production but we can support them.
  E-VPN: multipoint to multipoint layer 2 MPLS VPNs: lab tested, production code upgrades needed.
  Presentation at : https://stats.uwsys.net/other/ [yes, this website is self signed, I am not trying to steal your credit card numbers]

## Slide 7
FIN