## Slide 1: MPLS on UW System Network
Michael Hare

## Slide 2: Purpose of presentation
As I didn't really understand MPLS going in, I thought it would be useful to share what I've learned in logical order [vs chronological order, which would leave you with a jumbled mess].
Note: My experience is Juniper specific so there may not be a 1:1 match in Cisco land.

## Slide 3: Overview
Prepare IGP for MPLS
Prepare BGP for MPLS
Enable MPLS
Deploy services
Keeping it running

## Slide 4: Preparing your IGP for MPLS
The MPLS layer is built upon your IGP, so you should take steps to make it robust. Steps include:
  Improving convergence in your IGP
  Securing your IGP

## Slide 5: Improving convergence in your IGP
The faster your IGP converges, the more robust your MPLS services will be.
Minimize devices in an area
Enable loop free alternate routes. An alternative route is calculated and installed in the forwarding table, moving convergence to near sonet levels.
  LFA route will not be able to calculate backups for 100% of LSA's: more on this later
    http://www.juniper.net/documentation/en_US/junos11.4/topics/topic-map/ospf-loop-free-alternate-routes.html
Eliminate/reduce links between routers that are not directly connected. If you can't, BFD is required.
  full disclosure: I run area 0 everywhere in uwsys.net.

## Slide 6: Improving convergence in your IGP [2]
Make sure your loopback resolution doesn’t match aggregate or default route. When you have a node failure this is required to withdraw unusable BGP routes in a timely fashion.
  set routing-options resolution rib inet.0 import limit-inet0-resolution
  set policy-options policy-statement limit-inet0-resolution term reject-routes from prefix-list-filter sync_lists-limit-inet0-resolution exact
  set policy-options policy-statement limit-inet0-resolution term reject-routes then reject
  set policy-options policy-statement limit-inet0-resolution then accept
  set policy-options prefix-list sync_lists-limit-inet0-resolution 0.0.0.0/0
  set policy-options prefix-list sync_lists-limit-inet0-resolution 143.235.0.0/16

## Slide 7: Securing your IGP
Keep your IGP rock solid
ISIS does not use IP, it uses CLNS. Not being world reachable adds a layer of security
Use routing engine filters to protect protocols, not just your IGP.
Do not run IGP protocols with your customers [sorry guys, its true].
IPSEC

## Slide 8: Preparing BGP for MPLS
MPLS VPNs use BGP as a database to distribute information.
  BGP/MPLS overview
  Preparing BGP for MPLS

## Slide 9: BGP/MPLS overview
BGP is used as the database is used to distribute VPN information
  Each BGP family [AFI/SAFI] have different NLRI that describes each database row. NLRI are per AFI/SAFI.
    http://www.iana.org/assignments/safi-namespace/safi-namespace.xhtml
    https://tools.ietf.org/html/rfc7432#page-13 [E-VPN NLRI]
note: point to point pseudowires can be built without BGP but everything else needs BGP.

## Slide 10: Preparing BGP for MPLS
BGP requires a full mesh with each BGP speaker in an AS. Route reflectors simplify device configuration by requiring a full mesh only with the route reflectors
  Use two [or more] devices as BGP route reflectors.
  Route reflectors can be inline or out of forwarding path
Enable all of the BGP families you think you want, because adding an NLRI to a peer requires a BGP peer reset.
  flowspec, l3vpn, ipv6 l3vpn, evpn/l2vpn
note: On uwsys.net I use two inline core devices for this function and have been satisfied

## Slide 11: iBGP BFD
iBGP sessions should –NOT- have BFD.
Instead, PE IGP loopback should be withdrawn during node outage, marking routes as invalid [not best path].
If node outage is brief [60 ~ 90s], BGP will not need to re-establish.
See “Improving convergence in your IGP … limit-resolution … “

## Slide 12: Enable MPLS
MPLS: Basic terminology
Label distribution [LDP, RSVP] and tunneling

## Slide 13: MPLS: Basic terminology
MPLS forwards packets by switching labels [push, pop] based on a forwarding database
  Label A on interface X: pop label A, push label B, forward on interface Y:
P: Provider core node.
PE: Provider edge: Node that connects directly to a customer network
CE: Customer edge: Does not participate in P/PE MPLS protocols, but is serviced by it. Generally outside of the service provider’s domain.
Note: UW System Network does not have a pure ‘P’ node. The MX2010s are both P and PE nodes as customers directly connect. In fully l3vpn’d networks, the P device could be absent all customer routes in the FIB, only using IGP and MPLS to forward packets.

## Slide 14: Label distribution [LDP, RSVP] and tunneling
LDP and RSVP are used to distribute labels between P/PE devices
Labels are distributed by sending LDP/RSVP control packets over IP.
P/PE devices are numbered by their IP loopback addressing
LDP and RSVP are commonly run on IPv4. However, LDP and RSVP do not forward packets, they setup MPLS routing databases. There are ways to forward IPv6 but only run LDP/RSVP over IPv4.

## Slide 15: LDP
LDP mirrors your IGP.
  MPLS traffic will follow your IGP path
  Juniper IGP LFA implementation extends to IGP, meaning an MPLS backup path between PE1 and PE2 can be precomputed and installed in forwarding table when possible.
LDP can automatically signal a full mesh of paths between P/PE, making it simple to configure
LDP neighbors are point to point but can be held up using their P/PE addressing. This feature is called session-protection.
  If point to point LDP session is interrupted but PE1 and PE2 are still unicast reachable, MPLS labels need not be discarded, improving convergence time upon restoration [in the same style as not running BFD on iBGP]
  As LDP is dependent on a converged IGP, use ldp-synchronization to make sure the IGP isn’t active until LDP is active.

## Slide 16: RSVP
RSVP can steer MPLS traffic in a way other than IGP best path.
RSVP can be configured as a dynamic backup to LDP for LDP paths that cannot calculate a LFA. In Juniper land, this is called “link-protection dynamic-rsvp-lsp”
RSVP ‘fast reroute’ is like LDP LFA but on steroids as it considers path constraints.
RSVP requires more work from the operator to be useful

## Slide 17: So do I use LDP or RSVP?
  LDP and RSVP can be run side by side.
LDP
  Pros: LDP keeps things simple with minimal config. A good place to start.
  Pros: Juniper implementation can use RSVP to augment LDP LFA.
  Cons: Lots of needless labels is inefficient [signaled backups between PEs that do not actually communicate, etc]
RSVP
  Pros: can be used for specific traffic engineering needs
  Cons: more ‘by hand’ configuration [automation!]

## Slide 18: Deploy services
Once IGP, BGP and MPLS is in place, deploy services
While this is probably the most exciting portion, it is omitted. See me for details. I have deployed or tested
  L2circuit [pseudowire]
  L2 E-VPN
  I have not deployed L3 VPN but it is similar to L2 E-VPN in config
  I have not deployed MPLS multicast

## Slide 19: Keeping it running
Use routing engine filters to protect protocols, not just your IGP.
  [IGP: OSPF, ISIS. MPLS: LDP, RSVP. BGP, BFD, IGMP, MSDP, PIM, VRRP. DNS, NTP]
Monitoring
  At a minimum, track BGP NLRI counts and watch syslog.
Configuration sanity management
  There are lots of config bits that need to align for this all to work well.

## Slide 20: That’s all, folks
FIN