## Slide 1: MPLS on UW System Network
Michael Hare

## Slide 2: Purpose of presentation
As I didn't really understand MPLS going in, I thought it would be useful to share what I've learned in logical order [vs chronological order, which would leave you with a jumbled mess].
Note: My experience is Juniper specific so there may not be a 1:1 match in Cisco land.

## Slide 3: Overview
Prepare your IGP for MPLS
Prepare BGP for MPLS
Enable MPLS
Deploy services
Keeping it running

## Slide 4: Preparing your IGP for MPLS
The MPLS layer is built upon your IGP, so you should take steps to make it robust. Steps include:
  Collapsing your IGP
  Improving convergence in your IGP
  Securing your IGP

## Slide 5: Collapsing your IGP
Carry IPv4/IPv6 a single IGP protocol such as ISIS or carry IPv4 routes inside of OSPFv3.
  less room for topology error [ passive/active -> metrics/mtu ]
  less cpu/resources to converge, run BFD, etc
full disclosure: in uwsys.net, I still run separate OSPFv2 and OSPFv3 sessions

## Slide 6: Improving convergence in your IGP
The faster your IGP converges, the more robust your MPLS services will be.
Minimize devices in an area
Enable loop free alternate routes. An alternative route is calculated and installed in the forwarding table, moving convergence to near sonet levels.
  LFA route will not be able to calculate backups for 100% of LSA's: more on this later
    http://www.juniper.net/documentation/en_US/junos11.4/topics/topic-map/ospf-loop-free-alternate-routes.html
Eliminate/reduce links between routers that are not directly connected. If you can't, BFD is required.
  full disclosure: I run area 0 everywhere in uwsys.net.

## Slide 7: Securing your IGP
Keep your IGP rock solid
ISIS does not use IP, it uses CLNS. Not being world reachable adds a layer of security
Use routing engine filters to protect protocols, not just your IGP.
Do not run IGP protocols with your customers [sorry guys, its true].

## Slide 8: Preparing BGP for MPLS
MPLS VPNs use BGP as a database to distribute information.
  BGP/MPLS overview
  Preparing BGP for MPLS
  iBGP BFD

## Slide 9: BGP/MPLS overview
BGP is used as the database is used to distribute VPN information
  Each BGP family [AFI/SAFI] have different NLRI that describes each database row. NLRI are per AFI/SAFI.
    http://www.iana.org/assignments/safi-namespace/safi-namespace.xhtml
    https://tools.ietf.org/html/rfc7432#page-13 [E-VPN NLRI]
note: point to point pseudowires can be built without BGP but multipoint layer 2 and layer 3 need BGP.

## Slide 10: Preparing BGP for MPLS
BGP requires a full mesh with each BGP speaker in an AS. Route reflectors simplifying device configuration by requiring a full mesh only with the route reflectors
  Use two [or more] devices as BGP route reflectors.
  Route reflectors can be inline or out of forwarding path
Enable all of the BGP families you think you want, because adding an NLRI to a peer requires a BGP peer reset.
  flowspec, l3vpn, ipv6 l3vpn, evpn/l2vpn
note: On uwsys.net I two inline core devices for this function and have been satisfied

## Slide 11: iBGP BFD
iBGP sessions are multihop, therefore require BFD
Otherwise, a route reflector client could take 60 to 90 seconds to timeout if a route reflector becomes unreachable.
This is very bad when iBGP has converged to a belief that the 'dead' route reflector is best path for a route.
Know your platform. point to point BFD is often done in forwarding linecard whereas multihop BFD is sometimes done at control plane.
Because it's done at control plane you may need longer timers if you are using nonstop routing.
I use 3x500ms for point to point BFD and 4x2500 for multipoint. 10s is less than 60s.

## Slide 12: Enable MPLS
MPLS: Basic terminology
Label distribution [LDP, RSVP] and tunneling

## Slide 13: MPLS: Basic terminology
MPLS forwards packets by switching labels [push, pop] based on a forwarding database
  Label A on interface X: pop label A, push label B, forward on interface Y:
P: Provider core node. In some networks, the P device could be absent all customer routes, only using IGP and MPLS to forward packets.
PE: Provider edge: Node that connects directly to a customer network
CE: Customer edge: Outside of the service provider’s domain. Does not participate in P/PE MPLS protocols, but is serviced by it.
Note: UW System Network does not have a pure ‘P’ node. The MX2010s are both P and PE nodes as customers directly connect

## Slide 14: Label distribution [LDP, RSVP] and tunneling
LDP and RSVP are used to distribute labels between P/PE devices
Labels are distributed by sending LDP/RSVP control packets over IP.
P/PE devices are numbered by their IP loopback addressing
LDP and RSVP are commonly run on IPv4. However, LDP and RSVP do not forward packets, they setup MPLS routing databases. So, you can forward IPv6 but only run LDP/RSVP over IPv4.
MPLS tunnel is just a fancy way of describing a signaled forwarding path between two P/PE devices.

## Slide 15: LDP
LDP mirrors your IGP.
  Juniper IGP LFA implementation extends to IGP, meaning a backup path between PE1 and PE2 can be precomputed and installed in forwarding table
LDP can automatically signal a full mesh of paths between P/PE
  Simple to configure
LDP neighbors are point to point but can be held up using their P/PE addressing. This feature is called session-protection.
  If point to point LDP session is interrupted but PE1 and PE2 are still unicast reachable, MPLS labels need not be discarded, improving convergence time upon restoration.
  As LDP is dependent on a converged IGP, consider ldp-synchronization to make sure the IGP isn’t active until LDP is active.
(Possible) con: MPLS traffic will follow your IGP path

## Slide 16: RSVP
RSVP can steer MPLS traffic in a way other than IGP best path.
  Juniper IGP LFA implementation extends to IGP, meaning a backup path between PE1 and PE2 can be precomputed and installed in forwarding table
RSVP can be configured as a dynamic backup to LDP for LDP paths that cannot calculate a LFA. In Juniper land, this is called “link-protection dynamic-rsvp-lsp”
RSVP ‘fast reroute’ is like LDP LFA but on steroids as it consider path constaints.
(Possible) con: RSVP requires more work from the operator to be useful

## Slide 17: So do I use LDP or RSVP?
  LDP and RSVP can be run side by side. We are currently doing so, although I may make a change.
LDP
  Pros: LDP keeps things simple with minimal config. A good place to start.
  Pros: Juniper implementation automatically uses RSVP to augment LDP LFA.
  Cons: Lots of needless labels is inefficient [label path BFD, signaling backups]
RSVP
  Pros: can be used for specific traffic engineering needs
  Cons: Slightly more ‘by hand’ configuration

## Slide 18: Deploy services
Once IGP, BGP and MPLS is in place, deploy services
While this is probably the most exciting portion, it is omitted. See me for details. I have deployed or tested
  L2circuit [pseudowire]
  L2 E-VPN
  I have not deployed L3 VPN but it is similar to L2 E-VPN in config
  I have not deployed MPLS multicast

## Slide 19: Keeping it running
Use routing engine filters to protect protocols, not just your IGP.
  [IGP: OSPF, ISIS. MPLS: LDP, RSVP. BGP, BFD, IGMP, MSDP, PIM, VRRP. DNS, NTP]
Monitoring
  At a minimum, track BGP NLRI counts
Configuration sanity management
  There are lots of config bits that need to align for this all to work

## Slide 20: That’s all, folks
FIN