## Slide 1: UW System Network Operations Metrics
Patrick Christian
8/10/2017

## Slide 2: FY16 Significant event summary
Marquette interchange crash into bridge wall (68 hrs)
BCN fiber cut north of Milwaukee impacted 4 UWCs (WashingtonCO, Manitowoc, SheboyganCO, WaukeshaCO) for ~13 hours (biz hours)
BCN configuration error impacted UWC-BarabooSaukCO for 8+ hours
UWEC Centennial Hall HVAC issues (resolved)
MX104 routing engine corruption (resolved)
Several campuses had (un)planned power events (UWC-Richland Center, UW-La Crosse, UW-Platteville, UWC-Sheboygan, UWC-Baraboo SaukCO)

## Slide 3: FY17 Significant event summary
MX104 corrupted flash memory at several locations
La Crosse – Tomah, Augusta fiber cuts (~8 hrs)
Several campuses had (un)planned power events (UW-Platteville, UW-Stevens Point, UW-River Falls, UWC-Marinette, UWC-Baraboo SaukCO, UWC-Waukesha)

## Slide 4: Workload metrics
Chart: Events per Fiscal Year
| FY15 | FY16 | FY17
Planned | 72 | 260 | 338
Unplanned | 130 | 88 | 111
* FY15 is a partial year
202
348
449
Notes: Increasing # of planned events
Unplanned events are roughly flat (25%) of total

## Slide 5: Overall network availability
FY16: 99.66% (with BCN)
FY16: 99.90% (w/o BCN)
FY17: 99.75% (with BCN)
FY17: 99.89% (w/o BCN
Availability = time all campus networks can
connect to UW-System Network

## Slide 6: FY16 campus network availability
Campus | Availability |  | Campus | Availability
UW-Eau Claire | 100% |  | UWC-Baraboo-Sauk County | 99.989%
UW-Green Bay | 100% |  | UWC-Barron County | 100%
UW-La Crosse | 100% |  | UWC-Fond du Lac | 99.966%
UW-Madison | 100% |  | UWC-Fox Valley | 100%
UW-Milwaukee | 100% |  | UWC-Manitowoc | 99.825%
UW-Oshkosh | 100% |  | UWC-Marathon County | 100%
UW-Parkside | 100% |  | UWC-Marinette | 99.994%
UW-Platteville | 100% |  | UWC-Marshfield | 100%
UW-River Falls | 100% |  | UWC-Richland Center | 99.994%
UW-Stevens Point | 100% |  | UWC-Rock County | 99.9996%
UW-Stout | 100% |  | UWC-Sheboygan | 99.841%
UW-Superior | 100% |  | UWC-Washington County | 99.853%
UW-Whitewater | 100% |  | UWC-Waukesha | 99.850%
Notes: BCN had some issues
Omits power outage at UW-La Crosse and HVAC failure at UW-Eau Claire as redundant connections were available

## Slide 7: FY17 campus network availability
Campus | Availability |  | Campus | Availability
UW-Eau Claire | 100% |  | UWC-Baraboo-Sauk County | 99.832%
UW-Green Bay | 100% |  | UWC-Barron County | 100%
UW-La Crosse | 100% |  | UWC-Fond du Lac | 99.968%
UW-Madison | 100% |  | UWC-Fox Valley | 100%
UW-Milwaukee | 100% |  | UWC-Manitowoc | 100%
UW-Oshkosh | 100% |  | UWC-Marathon County | 100%
UW-Parkside | 100% |  | UWC-Marinette | 99.993%
UW-Platteville | 100% |  | UWC-Marshfield | 100%
UW-River Falls | 100% |  | UWC-Richland Center | 100%
UW-Stevens Point | 100% |  | UWC-Rock County | 100%
UW-Stout | 100% |  | UWC-Sheboygan | 100%
UW-Superior | 100% |  | UWC-Washington County | 100%
UW-Whitewater | 100% |  | UWC-Waukesha | 99.953%
Notes: BCN had some issues
Omits power outages at UW-Platteville and River Falls as redundant connections to UW-System Network were available

## Slide 8: Root cause analysis
Chart: Frequency distribution of network event root causes
| Fiber | Facilities | CPE | Operations | Hardware | Circuits | Software | Misc
FY15 | 56 | 40 | 30 | 20 | 19 | 18 | 15 | 4
FY16 | 141 | 21 | 46 | 2 | 28 | 64 | 39 | 7
FY17 | 202 | 25 | 21 | 5 | 23 | 122 | 32 | 19
* FY15 is a partial year
Notes: Significant road work near Janesville, Rockford and the Michigan U.P. caused frequent commercial circuit events

## Slide 9: Questions?
  patrick.christian@wisc.edu