## Slide 1: Fall 2017 update Layer2+ Network Update
Michael Hare
uwsys.net
August 2017
https://stats.uwsys.net/graphs.html

## Slide 2: Total internet access: [excludes UW Madison research traffic]
relatively flat growth

## Slide 3: Transit [~8.1% in, ~23.3 out]
Well within our commits with Telia [2G] and Level3 [2G]

## Slide 4: Peering [~86% in,~55% out]

## Slide 5: Availability
(all outages: planned or unplanned, uwsys.net or 3rd party transport)

## Slide 6: Backbone updates
Currently in process of shifting high bandwidth UW Madison research traffic back to a dedicated 100G protect path (discrete from uwsys.net routers)
Deployment of new PE at Pyle Data Center for UWC
Telia and WRIPS access outside of BOREAS, for now

## Slide 7: General network improvements: mx104
mx104 recovery
  Mx2010 RE ships with CF for boot and SSD for /var, SSD can be used as secondary boot device
  Mx104 RE ships with NAND for boot and /var, no backup
  Multiple issues of NAND corruption discovered upon boot = sha1 checksum fail = stuck in bootloader
  Dual RE deployment decreases odds of catastrophic outage but doesn’t resolve problem
  Mx104 has two front facing USB ports: they can be used as storage with USB sticks
  Three lab mx104s running on USB for several months, bringing us reliability seemingly closer to that of a larger MX.
  If USB stick is installed it is treated as the primary boot device and NAND is used for /var; still trying to swallow the idea of booting from a $8 USB stick.

## Slide 8: General network improvements: Cisco
Discovered that Cisco 4500X were clearing MPLS EXP QoS bits by default (but left DSCP untouched). Caused some unexpected outages during DoS attacks against UWCs behind BCN. Resolved with a single command [NS-2740]
Disabled Cisco (not so) Smart Install on the 4500X and 1921 terminal servers: disabled telnet while I was at it (finally!) [NS-3069]

## Slide 9: New MPLS services
Additional VPNs between UWW and other campuses for VOIP service [UWGB, UWOSH]
UW LAX DR to UWRF
UWC DR to UWC Barron
L3VPN support: we’ve seen at least one loop in a production e-vpn deployment that was caused by an LACP configuration mismatch on the service provider side. Because of this incident I encourage the use of L3VPN instead of E-VPN where possible.

## Slide 10: Minimizing the impact of planned work
Previous workflow: announce window, perform maintenance, tolerate 60~90s of convergence fun. However, 2017/06/14 linecard upgrades on r-uwmilwaukee-hub caused significant (5 to 10 minute?) blackholing due to slow RIB/FIB convergence
As a result we tested a zero/low impact planned maintenance workflow during 2017/07/15 r-uwmadison-hub maintenance.
A bit of impact (a minute or two) during that event, refinements to be tested for 2017/08/12 r-uwmilwaukee-hub maintenance.

## Slide 11: Minimizing the impact of planned work (more)
Setting the IGP overload bit to discourage transit traffic via the device undergoing maintenance
Withdrawing advertisement of default route (if applicable)
Setting customer and peer/transit BGP sessions to reject all incoming routes
Juniper configuration groups make this about 6 lines to copy/paste regardless of # of peers.
As part of this work BGP import/export policies are now also sanity checked (I found several hilarious errors in the process)
iBGP remains up for device management

## Slide 13: Fall 2017 update Network Issues and Possibilities
Michael Hare
uwsys.net
August 2017

## Slide 14: Convergence problems during unplanned events
In May 2017 there was a multi hour transport issue affecting connectivity, amongst other things, between r-uwmadison-hub and Minneapolis.
Level3 access via shared 10G via AS2381 switch
MICE access via dedicated 10G to MICE aggregation switch
End result: hundreds of link flaps between r-uwmadison-hub and Ethernet switches that went on for hours

## Slide 15: Convergence problems during unplanned events (continued)
Major problem: No loss of link to Level3 router = Level3 router gleefully keeps forwarding traffic despite lack of end to end connectivity. Same problem with some MICE peers.
Some (partial) solutions deployed
  BFD and RTBH via Level3 wasn't working for us or AS2381. I worked with our colleagues in AS2381 to resolve. v6 BFD not supported by Level3 (ancient JunOS?) so this problem continues to exist for IPv6.
  MICE has deployed BFD on their route servers
  Optical protection enabled for 10G link to Level3 in Minneapolis and 10G link to MICE peering exchange in Minneapolis, but link failure between shared switch and provider could still cause convergence issues.

## Slide 16: Convergence problems (observations, solutions)
While BFD is good, it is best to keep the neighbor up
  Ingress loss of a full table peer is computation expensive.
  Egress loss of a transit/peer creates global churn
If you’re going to lose a peer, loss of link is required for fast convergence
  No loss of link means the directly connected subnet stays up (aka your next hop). The FIB doesn’t get updated and your packets head out an Ethernet segment with no end to end connectivity until the RIB can choose a new best route and install (update) the FIB

## Slide 17: Convergence problems (partial solutions)
More routes + more topology changes = more CPU time required
  Reducing the number of full table peers coming into our MX2010s
  Cleanup/consolidation of Internet2/TRCPS sessions enabled by their recent router deployments

## Slide 18: Convergence problems (remaining questions)
Aggregate default route creation a factor?
  A non zero number of uwsys.net connectors are multihomed to more than one provider. We generally don’t accept default route from transit because we’d prefer to throw away traffic to unallocated IPs ourselves.
  However, many connectors are reliant on default route so I need to advertise default when I think I have a full transit view.
  I am synthesizing a default route based on RIB conditions but I don’t know how computationally expensive this is.

## Slide 19: Convergence problems (aggregate route)
m7h@r-uwmadison-hub-re0# show routing-options rib inet.0 aggregate … route 0.0.0.0/0 { policy generate-default; as-path { origin incomplete; aggregator 65400 143.235.32.1; } discard; } | term generate-default { from { protocol bgp; as-path-group transit-providers; route-filter 0.0.0.0/0 prefix-length-range /8-/10; } then accept; } then reject; m7h@r-uwmadison-hub-re0# show policy-options as-path-group transit-providers as-path LEVEL3 "^3356 .+"; as-path TELIA "^1299 .+";

## Slide 20: Convergence problems (aggregate route)
m7h@r-uwmadison-hub-re0# run show route 0.0.0.0/0 detail inet.0: 648313 destinations, 3665443 routes (647812 active, 34 holddown, 845484 hidden) 0.0.0.0/0 (4 entries, 1 announced) … Contributing Routes (38): 12.0.0.0/8 proto BGP 12.0.0.0/9 proto BGP 12.128.0.0/9 proto BGP 15.0.0.0/8 proto BGP 16.0.0.0/8 proto BGP … | 

## Slide 21: Convergence problems (monitoring load)
It is costly (code development time) or impossible to get some stats via SNMP so the new fad is to snarf XML/JSON over SSH/SSL.. Bad news, higher CPU demand on router control plane.
New stats: per process CPU usage, load average, FIB update queue depth, etc
I believe the 2017/06/14 blackholing was exasperated by the incorrect collection of FIB update queue depth via “show krt queue” instead of “show krt state”. As the FIB queue depth got bigger so did the output of “show krt queue”. Ooops.

## Slide 22: Convergence problems (monitoring load)
Best guess, monitoring load is ~11% of CPU on MX2010

## Slide 23: Convergence problems (load average)
Load average during 2017/07/15 planned maintenance
Our MX2010 RE have four cores but …. 

## Slide 24: Convergence problems (load average)
“legacy” JunOS runs on FreeBSD. Multicore FreeBSD not supported until JunOS 15.X. We are running 14.1. While our MX2010 RE have four cores, all JunOS processes are sharing a single CPU core.
RPD process handles all routing update tasks and shows evidence of starvation during major topology changes.
We are looking at deploying FreeBSD based JunOS 16.1 this winter (on the MX2010s) to take advantage of the four cores. Tried 16.1 in the lab this summer, didn’t like what we saw.
Future JunOS may split BGP out of RPD for further parallelization
Load average and per process data during incidents indicates this could be meaningful improvement

## Slide 25: Convergence problems (bgp add-path)
We need to better understand internet facing use of bgp add-path.
bgp add-path has many modes, but a simple mode is to rerun the bgp best path selection algorithm N times, whereas N is how many paths you want to precompute and share with your iBGP neighbors.
The theory is precomputation is good when you are fully converged. The practice is that this really slows down convergence during cold boot.
Precomputation is all in the RE inside RPD, which we know is resource starved at times.
I have disabled add-path send on the mx2010 "internet routes" iBGP sessions by adding a policy for which routes were eligible [Deny-All]. I have left it enabled as-was for the internal iBGP (customer routes) so we should still realize add path benefits for routing to/from customers including the stability improvements for eBGP announcements this causes.

## Slide 26: Convergence problems (what else)
JunOS telemetry = push stats. Presumably lower control plane utilization? This is in its infancy and will require examination over the next few years
Route reflectors? JunOS can run on commodity hardware (or a VM) so best path calculation could be handed off to the fastest possible commodity core (flops) available?
Topology change: More, smaller devices closer to transit/peers (currently Chicago, Minneapolis)
  May not be able to rely on optical protection in the future. Routers closer to internet transit/peers pushes redundancy at layers 2.5/3
  Less fiber miles = less topology changes .. ? = less route churn = fewer convergence issues?
  Collapsing PE, P and Border onto same box saves money and presents issues that prevent us from taking advantage of some topology possibilities (MPLS P, BGP PIC Core)
  CPU demand to poll a smaller device is less because there are less datapoints to gather

## Slide 27: Convergence problems (what else)
More direct interconnects (less Ethernet switches in the middle)
  Loss of link to neighbor results in faster convergence
  Shared Ethernet switch is a cost saving technique
  Reliability goes up a bit, cost goes up a lot?
Multihome to two transit providers?
  Realistically we are single homed to two different providers
  Telia: r-uwmadison-hub and r-uwmilwaukee-hub but folded at 710NLSD, ethernet switch in the middle
  Level3: r-uwmadison-hub optically protected to Minneapolis, Ethernet switch in the middle.
  Losing the last link to a peer is more disruptive than losing 1 of N.

## Slide 29: Fall 2017 update Tools Update
Michael Hare
uwsys.net
August 2017

## Slide 30: Nothing major: a few minor improvements
Network user (net) ssh key hardening
VM environment changes at UW Madison
Adoption of git and packaging inside Network Services (slowly working towards packaging software)
Totally unrelated stuff: infoblox rollout on campus
gnmis search saving

## Slide 31: gnmis search saving