## Slide 1: UW System Network Operations Metrics
Patrick Christian
8/21/2018

## Slide 2: FY18 Significant event summary
Difficult to resolve fiber issues between:
  UW-Madison<->Watertown
  Wauwatosa<->UW-Milwaukee
  UW-Milwaukee<->Kenosha
MX104 corrupted flash memory at several locations
BCN (FY19 BadgerNet) reliability issues continue
Facility (power/cooling) issues at several UWCs & certain 4-year locations
Serious flooding in Northern WI did NOT impact UWC-Barron & UW-Superior connectivity

## Slide 3: Workload metrics
Chart: Events per Fiscal Year
| FY15 | FY16 | FY17 | FY18
Planned | 72 | 260 | 338 | 348
Unplanned | 130 | 88 | 111 | 260
* FY15 is a partial year
202
348
449
608
Notes: Increasing # of unplanned events (double v FY17) (fiber & facilities in FY18)

## Slide 4: Overall network availability
Availability = time all campus networks can connect to UW-System Network
 |  | FY16 | FY17 | FY18
Availability with BCN |  | 99.66% | 99.75% | 99.59%
Availability w/o BCN |  | 99.90% | 99.89% | 99.91%

## Slide 5: FY18 campus network availability
Campus | Availability |  | Campus | Availability
UW-Eau Claire | 100% |  | UWC-Baraboo-Sauk County | 99.9977%
UW-Green Bay | 100% |  | UWC-Barron County | 100%
UW-La Crosse | 100% |  | UWC-Fond du Lac | 99.995%
UW-Madison | 100% |  | UWC-Fox Valley | 100%
UW-Milwaukee | 100% |  | UWC-Manitowoc | 99.9994%
UW-Oshkosh | 100% |  | UWC-Marathon County | 100%
UW-Parkside | 100% |  | UWC-Marinette | 99.998%
UW-Platteville | 100% |  | UWC-Marshfield | 100%
UW-River Falls | 100% |  | UWC-Richland Center | 99.9926%
UW-Stevens Point | 100% |  | UWC-Rock County | 99.7433%
UW-Stout | 100% |  | UWC-Sheboygan | 99.9994%
UW-Superior | 99.9949% |  | UWC-Washington County | 99.9408%
UW-Whitewater | 100% |  | UWC-Waukesha | 99.9977%
 |  |  | UWC-Online | 99.9885%
 |  |  | UWC-Upham Woods | 99.9455%
Notes: 3rd party circuit providers (e.g. BCN had some issues v dark fiber to campus

## Slide 6: Root cause analysis
Chart: Frequency distribution of network event root causes
| Fiber | Facilities | CPE | Operations | Hardware | Circuits | Software | Misc
FY15 | 56 | 40 | 30 | 20 | 19 | 18 | 15 | 4
FY16 | 141 | 21 | 46 | 2 | 28 | 64 | 39 | 7
FY17 | 202 | 25 | 21 | 5 | 23 | 122 | 32 | 19
FY18 | 303 | 53 | 28 | 21 | 32 | 112 | 51 | 8
* FY15 is a partial year
Notes: ~50% of events continue to be fiber related
Facilities issues slight uptick

## Slide 7: Questions?
  patrick.christian@wisc.edu