## Slide 1: FY19 UW System Network Operations Metrics
Patrick Christian
9/24/2019

## Slide 2: FY19 Significant event summary
MX104 corrupted flash memory at several locations
  Replacement project complete!
BadgerNet reliability issues continue
  Marinette down ~80 hours in FY19!
Facility (power/cooling) issues at several branch campuses – will address power in SysNet2020
Serious flooding in Western WI did NOT impact Richland Center, UW-La Crosse & UW-Platteville connectivity

## Slide 3: Workload metrics
Chart: Events per Fiscal Year
| FY15 | FY16 | FY17 | FY18 | FY19
Planned | 72 | 260 | 338 | 348 | 269
Unplanned | 130 | 88 | 111 | 260 | 361
* FY15 is a partial year
202
348
449
608
630
Notes: Increasing # of unplanned events (double v FY17) (fiber & facilities in FY18)

## Slide 4: Overall network availability
Availability = (unplanned) time all campus networks can connect to UW-System Network

## Slide 5: FY19 campus network availability
Campus | Availability |  | Campus | Availability
UW-Eau Claire | 100% |  | UW-Baraboo-Sauk County | 99.8141%
UW-Green Bay | 100% |  | UW-Barron County | 100%
UW-La Crosse | 100% |  | UW-Fond du Lac | 100%
UW-Madison | 100% |  | UW-Fox Valley | 100%
UW-Milwaukee | 100% |  | UW-Manitowoc | 99.9893%
UW-Oshkosh | 100% |  | UW-Marathon County | 99.9994%
UW-Parkside | 100% |  | UW-Marinette | 99.0891%
UW-Platteville | 100% |  | UW-Marshfield | 99.9989%
UW-River Falls | 100% |  | UW-Richland Center | 99.9621%
UW-Stevens Point | 99.9994% |  | UW-Rock County | 99.9536%
UW-Stout | 100% |  | UW-Sheboygan | 99.8925%
UW-Superior | 99.9994% |  | UW-Washington County | 99.9566%
UW-Whitewater | 99.9715% |  | UW-Waukesha | 99.9888%
 |  |  | UWC-Online | 100%
 |  |  | UWC-Upham Woods | 99.9127%
 |  |  | UW Colleges-Ext (780) | 99.9654%
Notes: 3rd party circuit providers (e.g. BadgerNet had issues v dark fiber to campus

## Slide 6: Root cause analysis
Chart: Frequency distribution of network event root causes
| Fiber | Facilities | CPE | Operations | Hardware | Circuits | Software | Misc
FY15 | 56 | 40 | 30 | 20 | 19 | 18 | 15 | 4
FY16 | 141 | 21 | 46 | 2 | 28 | 64 | 39 | 7
FY17 | 202 | 25 | 21 | 5 | 23 | 122 | 32 | 19
FY18 | 303 | 53 | 28 | 21 | 32 | 112 | 51 | 8
FY19 | 217 | 76 | 43 | 19 | 42 | 115 | 73 | 0
* FY15 is a partial year
Notes: ~50% of events continue to be fiber related
Facilities issues slight uptick

## Slide 7: Questions?
  patrick.christian@wisc.edu