## Slide 1: Wireless - Core
Routing:
  2 Separate locations
  2 Cisco Nexus 7706 switches with Fab3 fabric cards and M3 line cards
  Uplink switch for all wireless core devices: controllers, firewalls, service switches(authentication, dhcp, monitoring)
  Router for all wireless management networks and all centrally managed wireless client networks (uwnet, eduroam, uwnet-wired, iot)
  Peered with the campus core
Firewall
  2 PA 5260 firewalls, active/standby

## Slide 2: Wireless - Controllers
Controllers:
  AOS 6.4.4.15
    Master/Standby + 2 local controllers
      4 Aruba 7240 controllers
      Supporting remaining ap-125 access points
  AOS 8.7.1.9
    MC1
      2 10K HW Mobility Conductor appliances
      9 Aruba 7240 controllers
      Primarily serving academic buildings
      Connected to legacy core switches
    MC2
      2 10K HW Mobility Conductor appliances
      8 Aruba 7280 controllers
      Primarily serving residential buildings

## Slide 3: Wireless –Net Services
ClearPass Policy Manager
  Cluster of 10 appliances (1 publisher, 1 standby publisher, 8 subscribers)
2 dedicated isc-dhcpd servers
Airwave
Netinsight
VMW Edge Network Intelligence
Aruba UXI sensors, NetBeez
Fido, GNMIS

## Slide 4: Wireless –Net Services
AP-125
AP-203H
AP-205H
AP-224
AP-225
AP-275
AP-303H
AP-318
AP-324
AP-325
AP-344
AP-345
AP-375
AP-503H
AP-505H

## Slide 5: Wireless - Clients

## Slide 6: Wireless - Traffic

## Slide 7: Wireless – FW Sessions

## Slide 8: Wireless – FW Sessions

## Slide 9: Campus Wireless Upgrade
Started in 2017
  Approximately 8000 AP’s for the entire campus
  Philosophy shifted from a “Coverage” model to a ”Density” model (move from emphasizing covering the largest area to supporting the most users)
Barriers
  ISP fiber (MM  SM), Added POE requirements, Edge switch upgrades, TR power requirements
  slow progress when using only campus resources for infrastructure upgrades
Currently supporting about 18000 AP’s with about 279 remaining AP-125’s

## Slide 10: Current Efforts
Replacing all 7240 controllers with 7280’s
Expanding both Mobility Controller domains to 10 controllers
Decommission the 6.4 environment
Instantiate 3rd Mobility Controller Domain to accommodate additional ap growth
Complete physical migration of all controllers to N7706 cores